## Slide 1: On Effective IDDQ Testing of Low-Voltage CMOS Circuits Using Leakage Control Techniques
ECE 7502 Class Discussion
W.P.M.R Pathirana
31st March 2015

## Slide 2
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Verify
Test
Test

## Slide 3: What is IDDQ testing?
IDDQ testing is simple method to identify the defects on IC based on the steady state power-supply current.
IDDQ(Measured)>IDDQ(Th) Defective
IDDQ flowing through inverter with and without defect[1]

## Slide 4: Problem statement
For new Technologies (Deep submicron levels)
Low threshold Transistors
Higher Leakage
IDDQ(Fault Free)≈IDDQ(Defective)
Test escapes and yield loss
A-test escapes
B-yield loss
Earlier Technologies[5]
Deep submicron Technologies[5]

## Slide 5: Source of Leakage
ID-Reversed biased diode junction leakage
Isub-Subthrehold leakage
IG-Gate oxide tunneling leakage
IGIDL-Gate induce drain leakage
IPT-Channel punch through current

## Slide 6: Source of Leakage
ID-Reversed biased diode junction leakage
  Minimized with the Shrinking transistor size
Isub-Subthrehold leakage
  Exponential relationship between sub threshold current and device threshold voltage
  Subthreshold leakage is the dominant
IG-Gate oxide tunneling leakage
  Contribute significantly to leakage as gate oxides are made ever thinner
IGIDL-Gate induce drain leakage
  Strong reverse bias of the gate and large drain-source voltage are required
IPT-Channel punch through current
  Short channel transistors operated at high drain source voltages
Neglected by Author for low voltage operation

## Slide 7: Leakage current model
γ'-Linearized body effect coefficient
  If Vs is small, body effect is linear and represent with γ’Vs
η-DIBL coefficient
μ0-Zero bias mobility
n-Subthrehold swing coefficient
  n = 1+ ξsitox/ξoxtsi
  ξ-permittivity and t-thickness of the depletion layer

## Slide 8: Leakage control techniques
CMOS NAND gate
Input vector 011,101,110
  Leakage is computed for NMOS which is turned off
Input vector 001, 010,110
  Two transistors turned off
  Positive Vs on NMOS will reults great reduction on leakage current

## Slide 9: Leakage control techniques(Input vector generation method)
For circuit with n primary inputs, there are 2n combination
Exhaustive method is limited to circuits with a small number of primary inputs
For large circuits, a random search based technique can be used
  Involves generating a large number of primary inputs
  Evaluating the leakage of each input
  Keeping track of the best vector giving the minimal leakage current
Employ genetic algorithm to exploit historical information to speculate on new search points with expected improved performance to find a near optimal solution
  More efficient compare to the random based technique

## Slide 10: Dual-Threshold Voltage Design
Leakage current can be minimized using multiple thresholds
  Exponential relationship between leakage current and threshold voltage in the weak inversion region
Multi threshold voltage CMOS (MTCMOS) circuit technology
  Reduce the standby leakage current by inserting high-threshold devices in series to normal circuitry
  Increased area and delay
For a logic circuit, dual thresholds can be employed to minimize the leakage power dissipation
  Assign hight Vt transistors to noncritical paths
  No area over head and performance degradation

## Slide 11: Dual-Threshold Voltage Design
The pseudocode of high-threshold voltage assignment in the dual-threshold design technique
Can reduce more than 50% of leakage using vector control techniques
Can reduce more than 80% of leakage with dual threhold design
The combination of both technology can reduce the leakage by a factor of 10

## Slide 12: Bridging Fault Model
Shorts can be divided into intragate shorts and intergate shorts.
90 % of the shorts can be intergate shorts
Bridging Fault can only be dectected
  Activating a direct conducting path from VDD to the ground
  Satisfying the IDDQ test limit
For the input of If the logic values for the inputs of the left and the right gates are “000” and “111” , bridging fault can be dectected

## Slide 13: Figure of Merit for IDDQ Testing
When X1=0 and X2=1,y1=y2=0.4 V at Vdd=1 V
Will results direct path current in the fanout gate (I2)
Short
At 1 V – I1- 99 μA and I2=15 μA
Vout,y3=0.9 V → Can be considered as logic 1
Direct path current can hardly be present unless another
bridging fault occurs
Even for the gates driven by the shorted gates ,If fanin numbers > 1,direct path may not occur and depends on logic inputs

## Slide 14: Figure of Merit for IDDQ Testing
IDDQ (faulty) definitions
IDDQ(faulty)= IDP+IDPfanouts+Isubothergates
Where IDP- the direct path current through the gates where shorts occur
IDPfanouts-the possible direct path current of the gates driven by the output of the shorted gates
Isubothergates-leakage current through all the other gates where direct paths are not present
Fault current ratio(FCR)= IDDQ(faulty)/IDDQ (fault_free)
If FCR is high → Higher accuracy in IDDQ testing

## Slide 15: Implementation and experimental results
Fault resistance value set to Zero ???
20 bridging faults are randomly introduced
20 test vectors are randomly generated
Calculate the
  FCRs-(Base line for comparison)-fault current ratio with a single low threshold
  FCRd-dual-threshold voltage technique fault current ratio
  FCRdv-dual-threshold voltage and vector control technique fault current ratio
Random search technique is used and select 20 out of 1000 vectors for FCRdv
FCRdv > FCRd>FCRs

## Slide 16: Implementation and experimental results
X-axis – Test vectors
If IDDQtest limit is 3
  40% and 70% of the bridging faults can be detected for the initial single low-threshold circuit and the dual-threshold circuit
If IDDQtest limit is 10
    0%, 20% and 40 % of the bridging faults can be detected for the initial single low-threshold circuit ,the dual-threshold circuit and Combining vector control technique

## Slide 17: Implementation and experimental results
The fault coverage for MCNC benchmark circuit i1
The FCR for MCNC benchmark circuit i1
FCR is high → fs,fd and fdv gave same results

## Slide 18: Implementation and experimental results
FCR is low → fs,fd and fdv gave very small test coverage
indicates that vector control and dual-threshold voltage techniques can not help testing of very large circuits working at a low supply voltage
The fault coverage for ISCAS benchmarks C6288
The FCR for ISCAS benchmarks C6288

## Slide 19: Implementation and experimental results
If IDDQ set to 10
  Dual-threshold voltage technique- 45 %
  Dual-threshold voltage technique + Vector control technique- 60 %
The fault coverage for ISCAS benchmarks
The FCR for ISCAS benchmark C3540

## Slide 20: Conclusion
The scaling of device threshold due to the scaling of supply voltage makes the fault-free current increase dramatically.
Reduce the feasibility of IDDQ testing for low voltage CMOS circuits
Vector control and dual-threshold techniques to reduce the intrinsic leakage current to benefit IDDQ testing
“vector control and dual-threshold voltage techniques can not help testing of very large circuits working at a low supply voltage”

## Slide 21: Discussion questions
How the assumption of bridge resistance settings to 0 is accurate?
How FCR can be related to defining the fault coverage percentage?
How can we implement this method in our research?
How can we generate random input vectors in cadence virtuoso?
How does the assumption of ignoring some source leakage components affect the final conclusion?

## Slide 22: Papers
[1] Chen, Zhanping, Liqiong Wei, and Kaushik Roy. "On effective I/sub DDQ/testing of low-voltage CMOS circuits using leakage control techniques." Very Large Scale Integration (VLSI) Systems, IEEE Transactions on 9.5 (2001): 718-725.
[2] M. C. Jeng, “Design and modeling of deep-submicrometer MOSFETS,”Electron. Res. Lab., Univ. California, Berkeley, Rep. ERL-M90/90,1990.
[3] L. Wei, Z. Chen, M. John, K. Roy, Y. Ye, and V. De, “Design and optimization of dual threshold circuits for low voltage low power applications,”IEEE Trans. VLSI Syst., vol. 7, pp. 16–24, Mar. 1999.
[4] J. P. Halter and F. Najm, “A gate-level leakage power reduction method for ultra-low-power CMOS circuits,” in Proc. IEEE Custom Integrated Circuits Conf., Santa Clara, CA, May 1997, pp. 475–478.
[5] Rajsuman, Rochit. "Iddq testing for CMOS VLSI." Proceedings of the IEEE 88.4 (2000): 544-568.

## Slide 23: Paper Map
[5] A survey on IDDQ Testing
[2] Leakage current model
Model for leakage
[3] dual threshold circuits
High vt assignment model
[4] Vector control techniques
Random search based method
[5] Final model for effective IDDQ test
Assigning different vectors to reduce leakage